4G Asset GPS Tracker

(G200L)

V 1.0

2020-10-17

Contents

1. Quick View	3

2. Parameters	4

3. Command List	5

4. How to use device?	6

5. How to Set working mode:	6

## Quick View

G200L is 0 installation magnet GPS tracker based on global 4G LTE frequency. With building GPS & microphone, device can be used for real time tracking or long time asset monitoring purpose. It also supports fall-off alarm in case device removed.

| Indicator | Light Status |
| --- | --- |
| Power ON/OFF开关/电源 | Insert SIM card power on, remove SIM power off插入SIM卡开启电源，取出关闭电源 |
| Red light红灯 | Power | Flashing: when charging; Constant on: charge full闪光: 充电时; 常亮: 充满电 |
| Green light | GPRS network | Flashing: failed to connect server; Constant on: connect server OK |
| Blue light | GPS signal | Flashing: failed to get GPS signal; Constant on: GPS located OK |
| Light will turn off after power on 3 minutes, make a call or send any SMS to wakeup light 10s shortly. |

## Parameters

| Size | 76.1*49.9*30.2mm |
| --- | --- |
| Frequency (Version option) | G200LN | EC-25 AFX (US/Canada/Mexico) | LTE-FDD: B2/B4/B5/B12/B13/B14/B66/B71 WCDMA: B2/B4/B5 |
|  | G200LE | EG912Y-EU (Europe/S.E Asia/Africa/Australia/New Zealand) | LTE-FDD: B1/B3/B5/B7/B8/B20/B28 LTE-TDD: B38/B40/B41 GSM: B2/B3/B5/B8 |
|  | G200LC | EC200S-CN (China/India/Brazil) | LTE-FDD: B1/B3/B5/B8 LTE-TDD: B34/B38/B39/B40/B41 GSM: 900/1800Mhz |
| GPS | Module | Quectel Module |
|  | Positioning mode定位方式 | GPS/BDS |
|  | Frequency频段 | GPS L1 1575.42 Mhz BeiDou 1561.098Mhz |
|  | Accuracy准确性 | < 5 M |
|  | Speed Accuracy | <0.1M/S |
|  | sensitivity | -162dBm |
|  | Positioning time | Cold start ≤32S Warm start ≤3S |
| Power | Input voltage | DC 5V/2A |
|  | Working Currency | 120 mA |
|  | Standby Currency | 10uA |
|  | Working temperature | -20℃~+65℃ |
|  | Storage temperature | -40℃~+85℃ |
|  | Battery | 3.7V/4500mAH |

## Command List

| SMS Function | SMS Command format | SMS example |
| --- | --- | --- |
| Please don’t type “+” “space”, password 123456. Preset Center Number first if need receive SMS alarm. Each SMS must reply “Set OK” represent command successfully. |
| Step 1 Set IP Port | adminip+password+space+IP Address+space+port number | adminip123456 www.gps228.com 8989 |
| Step 2 Set APN | apn123456+space+LocalApn+space+ApnName+space+ApnPassword | apn123456 tim.br tim tim |
| Get Google link | smslink123456 |  |
| Set fall-off alarm | remove123456+space+1 | remove123456 1 |
| Cancel fall-off alarm | remove123456+space+0 | remove123456 0 |
| Set Time Interval | ITV123456+space+time interval(s) | If 60s , send SMS: ITV123456 60 |
| Set center number | centernum123456+space+phone number | centernum123456 13712345678 no need put country code |
| Cancel center number | centernum123456 | Center number use to receive alarm message |
| Set low battery alarm | lowbat123456+space+1 | lowbat123456 1 |
| Cancel low battery | lowbat123456+space+0 | lowbat123456 0 |
| Set SMS time zone | timezone123456+space+(timezone*60) | If+5.5:timezone123456 330 |
| Check device status | check123456 | check GPS GSM status |
| Check current mode | *SPJLX*P:123456*RM:0# |  |
| Restart device | reset123456 |  |
| Set alarm mode | KC123456+space+1 | APP alarm (default) |
|  | KC123456+space+2 | APP+SMS alarm |
|  | KC123456+space+3 | APP+SMS+PhoneCall alarm |
| Set vibrate alarm | vibrate123456+space+1 | Must keep continuously static 3 minutes before vibration |
| Cancel vibrate alarm | vibrate123456+space+0 |  |
| Set factory mode | begin123456 | It will erase all setting |

Tips: Fall-off alarm: device sticking to the metal cover with magnet, fall-off alarm will be triggered once device was removed off.

## How to use device?

Step 1: To power on the device, insert 4G GSM SIM card (Nano Size) with GPRS data activated. Make sure remove PIN code if SIM card need.

Step 2: Edit SMS Command send to device SIM number as below one by one

Set IP Port: adminip123456(space)www.gps228.com(space)8989

Set APN: apn123456(space)APN (space)ApnName(space)ApnPassword

Step 3: Go outdoor and keep device vibrating for 5 minutes for get accurate positioning, especially when 1st time using.

Step 4: Login Platform/APP:

Web:  www.secumore1818.com

Android & IOS APP: secumore1

Default to use IMEI number login, password 123456.

## Set working mode

A.) Mode 0: Real time tracking mode

- Command: *SPJLX*P:123456*RM:1,0#

- 0: means working mode 0.

B.) Mode 1 (default) : Power saving mode

Command: *SPJLX*P:123456*RM:1,1,3,3,120,30,3,30#

- 1: means working mode 1.---- User can modify yellow value as per actual needs.

- When device moving, it will update new location at every 1 minute;

- If not moving, device will sleep to save power & wake up for 3 minutes(above yellow 3) at every 120 minutes(above yellow120). Device will show disconnect from server when in this case.

C.) Mode 2: Set clock mode

- Command:*SPJLX*P:123456*RM:1,2, 3,1:00,2:00...#

- 2: means working mode 2. ----User can modify yellow value as per actual needs.

- Device will wake up for 3 minutes (above yellow 3) at fixed time clock 1:00,2:00 etc…

In Mode 2, Device will disconnect from server when sleep.

Tips: In all working modes, device standby time is directly affected by “working time”, if works longer, battery standby time will be shorter.