重要提示,请认真阅读

- 本个人应急通讯器是设计用于人员或贵重物品的定位通讯，对侵犯他人隐私的行为概不负责。

- 所有GPS定位相关的产品都会因外在因素产生误差，因此本机提供位置信息仅供参考。

- 因为电信运营商的缘故，在部分情况下，信息传送可能会延迟，本公司对使用者的人身和财产安全免责。

主要功能

- GSM四频 +GPS全球定位

- 网站平台/苹果/安卓/微信/SMS查询位置信息

- 轨迹回放

- 电子围栅

- SOS求救

- 一键拔号

- 来电来音+震动提醒

- 双向高保真语音通话

- 静音关怀

- 低电量报警

- 换卡提示

产品规格

GSM频段: 850/900/1800/1900MHz

GPRS标准: Class 12, TCP/IP

GPS定位时间: 冷启动 30sec(开阔天空)

温启动 29sec(开阔天空)

热启动 5sec (开阔天空)

GPS定位精度: 10-15米(开阔天空)

工作温度: -20℃ ~ +70℃

工作湿度: 5% ~ 95% RH

尺寸: 40.0(长)x34.0(宽) x14.0(高)毫米

重量: 27克

配件：

主机一台

充电器一个

USB充电线一条挂绳

说明书一本

产品示意图

| 编号 | 功能 | 编号 | 功能 |
| --- | --- | --- | --- |
| 1 | 重启复位孔 | 2 | 开/机关键 |
| 3 | USB充电口 | 4 | 1号按键 |
| 5 | GSM指示灯 | 6 | SOS按键 |
| 7 | GPS指示灯 | 8 | 2号按键 |
| 9 | 收音孔 | 10 | Ｍicro SIM卡槽 |
| 11 | 喇叭出音孔 | 12 | 挂绳孔 |

使用前准备:

本产品使用GSM网络的Micro-SIM卡(iphone4同类型)。并请注意以下事项:

- 在安装或取出SIM卡前，请先关机；

- 定位通讯器SIM卡需要开通GPRS和来电显示功能.

开/关机

请按胶塞上的指示方向插入Micro-SIM卡.

按开机键3秒,指示亮灯并伴有开机铃声,开机成功.

开机状态，按开机键3秒钟，指示亮灯并伴有关机铃声，则关机成功．

指示灯说明:

| 灯 | 功能 | 慢闪 | 快闪 | 灯灭 |
| --- | --- | --- | --- | --- |
| 蓝色 | GPS指示灯 | GPS定位中 | 定位成功 | GPS休眠 |
| 黄色 | GSM指示灯 | GSM搜网 | 搜网成功 | GSM休眠 |

智能手机APP绑定及功能设置

- 扫描说明书封底二维码下载APP手机客户端．

- 输入10位数ID号码，初始密码为123456，即可登录．

- 确认设备在线，即可进行对应的指令设置．

- 实时追踪:实时显示设备最新的定位位置.

- 历史轨迹:分时段查看设备的历史轨迹.

- 电子栅栏:设置或者取消电子栅栏区域.

- 设备消息:显示设备的报警列表.

- 报警提醒:是否接收报警信息的APP推送.

- 注销:退出APP程序,不再接收APP的报警推送,

以下特别说明:设置指令模块

5.接听模式:

- 静音模式:所有已设定的5个号码拔打RF-V16号码,,在不响铃声的状态下,远程收听RF-V16周围的声音,但不能与RF-V16使用者直接通话.

- 自动接听模式:所有已设定的5个号码拔打RF-V16号码,在响一声铃声后,远程收听RF-V16周围的声音,并可以与RF-V16持有者直接通话.

- 手动接听模式:任意号码拔打RF-V16号码,,必须要RF-V16持有者手动按键之后,才能与RF-V16持有者进行通话.

6.短信语言设置：选择短信报警的语言种类，本产品提供三种语言模式：中文，英文及法语

7.防骚扰模式：在手动接听模式下，是否允许陌生号码呼入．

8.时区：出厂默认为UTC+8北京时间，如果出国使用可跟据当地时区进行设置．

更多APP及平台详细功能请登录www.gsp123.org了解!

RF-V16也可接受短信方式设置相关的参数.

所有指令中的字母全部小写,标点为英文标点,并且都以#号为结束符.

绑定SOS1号码:短信指令:密码,sos1,手机号码#

例如:123456,sos1,180********#

定位通讯器即回复:已设置180********为主控号码。

特别提示:其他短信指令必须由SOS1号码设定.

其他短信指令表:

| 短信指令 | 功能 |
| --- | --- |
| 密码,t,新密码# | 更改密码,出厂密码123456 |
| 密码,sos1,号码# | 设置主控号码 |
| sos2,号码# | 设置sos2号码,其他号码以此类推 |
| callvib,1# | 来电震动开启(出厂默认） |
| Callvib,0# | 来电震动关闭 |
| aj# | 按键接听来电(出厂默认) |
| mt# | 免提自动接听来电 |
| jy# | 静音关怀 |
| dw# | 查询定位通讯器位置 |
| dsp# | 查询设备工作状态 |
| lag,1# | 系统语言转为中文.(出厂默认) |
| lag,2# | 系统语言转为英文. |
| lag,3# | 系统语言转为法文. |
| tim,数字# | 更改定时定位的间隔,单位为分钟. |
| gon# | 开启定位 (出厂默认) |
| goff# | 关闭定位 |
| lon# | 指示灯打开(出厂默认) |
| loff# | 指示灯关闭. |
| dndoff# | 防骚扰关闭。（出厂默认） |
| dndon# | 防骚扰开启。 |

注意事项

- 关机状态下,充电将自动开机.

- 请将本品安放在网络信号较好的位置使用。

- 新机使用前需充电2-3小时，以达到最佳的效果，充电时请使用本机配送的充电器，以免损坏主机。充电状态：红灯亮为充电中，绿灯常亮为充满电。

- 待机时间:1)每10分钟上传一次定位信息,待机时间为50小时，通话：5-8小时。(实测); 2)关闭定时上传定位信息,待机时间为300小时,约12天.注:以上数据来自GSM网络信号强的状态.

- 本机在开机或追踪状态下,搜网不成功或没有插放SIM卡,会自动重启.

- 本产品不防水,请在使用时注意防水.

- GPS数据上传间隔时间，出厂默认设置为：10分钟。

常见问题:

问:设备插卡后,能接通电话,但是在平台及APP上显示未启用.

答:请确认SIM卡已经开通了GPRS功能.

问:在防骚扰模式下,任何电话都能呼入.

答:A.请确认SIM已经开通了来电显示功能.

B.如果SOS号码与RF-V16卡号之间有绑定短信,设置时请使用短号设置.

问:设备显示在线,但用APP设置指令时,显示等待设备应答.

答: A.设备信号不良,导致GPRS通讯不畅通;

B.设备正在通话中.

问:设备SIM卡已经开通了GPRS功能,但是APP依然显示未启用.

答:因为移动和联通升级3G和4G后针对不同的SIM卡有不同的APN. 可能是预设GPRS的APN参数不正确.

请先用短信方式绑定SOS1号码,然后再发送短信指令:

联通卡:apn,uniwap#,重启后依然不行则改发:apn,uninet#

移动卡:apn,cmwap#,重启后依然不行则改发:apn,cmnet#

User Manual

GPS tracker & SOS communicator

Important, please attention:

1. This tracker was designed for people and asset location and communication, our company assumes no liability or responsibility for any behaviors violate other individual’s privacy.

2. Due to external factors all GPS devices have position error, so the position provide by this device just for reference only.

3. There may be delays caused by telecom operators at certain circumstance. Our company doesn’t assume liability for users’ personal and property safety

Main Features:

- GSM quad band network, all global GPS location

- Tracking Via website/IOS APP/Android APP/We chat/SMS

- Push button SOS alarm

- Click to call

- Ring tone+ Vibrate alert

- Two way Hi-Fi audio communication

- Hand-free talk

- Activity monitor

- Low battery alarm

- SIM changing alarm

Accessories

1* Main Host

1* Charger

1* Multiple-function USB cable

1* User manual

1* Necklace Style Lanyard

Product specification:

GSM network: 850/900/1800/1900MHz

GPRS standard: Class 12, TCP/IP

GPS locating time:

- 30sec with cold boot (open sky)

- 29sec with warm boot (open sky)

- 5sec with hot boot (open sky)

GPS positioning accuracy: 10-15m

Working temperature: -20℃ ~ +70℃

Working humidity: 5% ~ 95% RH

Host size: 40x34 x14mm

Host weight: 27g

Product View:

| Item | Function | Item | Function |
| --- | --- | --- | --- |
| 1 | Reboot hole | 2 | Power on/off |
| 3 | USB charger hole | 4 | Button 1 |
| 5 | GSM indicator light | 6 | SOS button |
| 7 | GPS indicator light | 8 | Button 2 |
| 9 | SIM card slot | 10 | Microphone |
| 11 | Loudspeaker | 12 | Hang rope hole |

Prepare for work:

Please choose GSM network-based Micro-SIM card (same as Iphone4) for the product. And please note:

a. Please be sure the tracker is turn off before insert or take out the Micro-SIM.b. Please be sure the GPRS and Caller id has been activated

Power on /off:

Please insert the Micro-SIM card into the card slot as directed.

Press the POWER key for 3 sec, then the tracker will ring and light on.

Indicator light show:

| Light Color | Function | Slow Flash | Fast Flash | Close |
| --- | --- | --- | --- | --- |
| Blue | GPS Indicator | GPS Searching | GPS Success | GPS Sleeping |
| Yellow | GSM Indicator | GSM Searching | GSM Success | GSM Sleeping |

APP binding and function setting:

- Scan the User manual back cover QR code to install the APP

- Enter the ID number and password to login, the default password is 123456.

- Confirm the device online, the corresponding instruction set can be achieved

- Real-time Tracking:show the last position and trace.

- Historical route:display the historical .

- Geo-fence: set and display geo-fence area,when the device get into or get out the geo-fence then it will send a alert SMS.

- Device message:display the alert list.

- Alarm setting:get the remind via APP when alarm

- Logout:logout the APP,and never get the alarm remind via APP.

- Setting

5.Answer Mode:

- Silent monitoring mode:

All have set 5 phone numbers dialing the device; you can remote listen to the voices around the device at the condition of no bell ring, but can’t speak to the device user.

- Auto answer mode:

All have set 5 phone numbers dialing the device, after a bell ring, you can remote listen to the voice around the device and speak to the user

- Push to talk mode:

Any number dialing the device number, only after the user press the button, you can speak to the device user

6.Language Setting：

Choose SMS language, the device provide three languages: Chinese, English and French

7.Do not disturb Mode:

In push-to-talk mode, whether to allow incoming strange number.

8.Time zones：

The factory default is UTC+08:00; users can set it according to local time zone.

Please log on http://www.gps123.org to learn more details of APP and platform

All functions also can set by SMS command

All command use in lowercase letters, without any blank space and ending by #.

Command for setting master number:

password,sos1,phone number#

For example:123456,sos1,180********#

The tracker will reply: 180******** has been set for the master number successfully.

Note:All SMS setting must send via SOS1 number.

| Command | Function |
| --- | --- |
| password,t,password | Change the password, factory default is 123456. |
| password,sos1, number# | Set master number |
| sos2(3,4,5), number# | Set sos2 number |
| callvib,1# | Turn on vibrate alert (factory default） |
| callvib,0# | Turn off vibrate alert |
| aj# | Set push to answer incoming call (factory default) |
| mt# | Auto-answer and hand free incoming call |
| jy# | Silence monitoring |
| dw# | Check the position |
| dsp# | Check the device work situation |
| lag,1# | Change the language to Chinese(factory default) |
| lag,2# | Change the language to English |
| lag,3# | Change the lauguage to French. |
| tim,digital# | Setting interval of the position data uploadthe unit is minutes |
| gon# | Turn on the tracking function(factory default) |
| goff# | Turn off the tracking function |
| lon# | Turn on the Indicator light (factory default) |
| loff# | Turn off the indicator light |
| dndoff# | Turn off DO NOT DISTURB in push-to-talk mode (factory default) |
| dndon# | Turn on DO NOT DISTURB in push-to-talk mode |

Command for SMS setting

Remark:

1. The tracker will boot automatically when it was charging.

put the tracker in network signal better position when use.

2. The new machines need to be recharged for 2-3 hours before use in order to achieve the best results, please use our distribute charger avoid damage to the host.

3. Standby time:

1) Upload location data every 10 minutes, the standby time is 50 hours, talking time is 5-8 hours (Actual test)

2) Turn off GPRS, the standby time is 300 hours, about 12 days .

Note: Above test data is under the status of strong GSM network

- Please charging and boot with SIM card, the device will automatically reboot when it can’t search GSM network.

- This product is not waterproof, please pay attention when using.

- GPS data upload time interval,factory default setting:10 minutes.

FAQ

Q: After inserting a SIM card, it can make a call, but it display not enable on the platform and APP

A: Please check that SIM Card has opened GPRS.

Q: In the DO NOT DISTURB mode, why any phone can call in?

A: Please check that SIM Card has opened caller ID.

Q: Device show online, but it shows “wait for the device responses” when you set instruction with APP.

A: a. Device signal is not good, so not smooth result of GPRS

b. Device is busy.

Q: The SIM card has opened GPRS function, but the device still not online

The tracker have pre-program all most APN, maybe the

APN of the SIM card you use don’t preset in the tracker,  please set SOS1 number first and then send command to add you APN into the tracker.

The command is: anp,<apn>#

# Text boxes

插卡说明

1.定位间隔:设置定位数据的上传密度,间隔越短待机时间也相应更短.

2.SOS1号码:对应1号按键号码,也是主控号码,用于发送指令及接收报警信息.

3.SOS2号码:对应2号按键号码.

4.白名单号码:S键求救及远程收听被授权的号码.

1.Locate interval: set the location data upload density, shorter standby time according to shorter interval.

2.SOS1 phone number: Button 1 phone number, also the master phone number, used to send command and receive alarm.

3.SOS2 phone number: Button 2 phone number, when you press button 2, the device will call the phone number.

4.White list number: the othe SOS number, also allow to remote listening