OBDII GPS TRACKER

USER MANUAL

PREFACE

Thank you for purchasing OBDII GPS tracker. This manual shows how to operate the device smoothly and correctly in details, please make sure to read this manual carefully before using the device. Please be noted that any update of the manual is made without prior notice. Each time the update of the manual will be released in the latest product sales. The manufacturer won’t assume any legal responsibility for any errors or omissions made in this manual.

1 SUMMARY

Working based on existing GPRS network and GPS satellites, this product can locate and monitor any remote targets by SMS, APP and Internet. It adopts the most advanced technology of GPS and AGPS dual positioning.

This device can directly connect with the car OBDII port. And detect vehicle failure & vehicle status through the APP.

| Content | Specs. |
| --- | --- |
| Dim. | 2G:47mm x 43mm x 20mm(1.85”*1.69”*0.79”) 4G:58mm x 45mm x 20mm（2.28”*1.77”*0.79”） |
| Weight | 2G:38g / 4G:55g |
| Network | 2G:GSM/GPRS 4G:FDD/WCDMA/GPRS |
| GPS sensitivity | -159dBm |
| GPS accuracy | 5m |
| Time To First Fix | Cold status 45s Warm status 35s Hot status 1s |
| Storage Temp. | -40°C to +85°C |
| Operation Temp. | -20°C to +55°C |
| Humidity | 5%--95% non-condensing |

| LED INDICATOR STATUS | MEANING |
| --- | --- |
| Yellow light -Solid | GPRS connection |
| Yellow light -Flash | No GPRS signal |
| Blue light -Solid | GPS connection |
| Blue light -Flash | No GPS signal |

How to find the OBD connector on your car:

There are 6places you may find the connector(most of car in 1 place)

How to install:

It is plug and play device, connect it to OBDII connector is ok.

- TURN ON THE DEVICE

Turn on the unit outdoors by inserting sim card, then the indicator light will on.

Insert the unit into the car OBDII port.
After waiting about 10-30seconds, you can use it and do any setting as the instructions of this manual.

Turn off the unit by removing the device from the OBD Port and taking away the sim card, then the indicator light goes out.

- SMS TRACKING

3.1.Admin number setting (After admin number setting, the device will reply the location message to the admin number when you dial the SIM card of the device.)

Command: admin123456 phone number（This phone number is your own mobile phone number , not the SIM card number in tracker .）

Reply：admin ok

E.g：admin123456 xxxxxxxxxx

When the unit is in over-speed alarm, shake sensor alarm, it will send alert to the admin number.（13265790180）

Admin number Canceling:

Command ：noadmin123456

Reply：noadmin ok

3.2. Send message “G123456#” to SIM card phone number in tracker , or call the SIM card phone number via the admin number, you will receive a Google Maps link of position.

E.g

EXPLANATION OF PARAMETERS/CODES IN SMS MESSAGE

- ID:8168000010  Device ID No. to log in APP and platform

- Spd:000  This refers to the device moving speed. The unit is km/h.

- T:13/10/15  15:55  Real-tracking time, the Default is London time. You can set language and time zone by SMS.

- Bat:100  The battery value is between 10% and 100%. Once it is less than 30%, it alarms.

- Google Link: This is the link to the Google map showing the position of the device.

3.3. Terminal (local) Time Setting(factory setting  GMT 0)

Command：timezone123456 local time zone

Reply：time ok!

E.g： timezone123456 +1     timezone123456 -1    Timezone123456 0

3.4. Over-speed Alarm setting

Over-speed Alarm setting:

Command ：speed123456 070（Suppose speed is 70km/h）

Reply：speed ok

When the unit speed is over 70km/h, it will send message “speed alarm!” to the admin number every 5 minutes.

Over-speed Alarm canceling ：

Command ：nospeed123456

Reply：nospeed ok

3.5. Shake sensor setting

Command：shock123456

Reply：shock ok

If there is no any alarms in 5 minutes, the unit will automatically set shake sensor alarm. In this case, it will  send message “sensor alarm!” to the master number when the unit get shake.

Shake alarm Canceling:

Command：noshock123456

Reply：noshock ok

3.6. Reset Hardware

Restore all settings to factory settings

Command：begin123456

Reply：begin ok

E.g：

4. START ONLINE TRACKING

4.1Set the APN for the tracker, then its online tracking by APP and platform works.

(Note:If you inserted the correct SIM Card and the device is online on the APP, no need to send the following APN setting commands.)

Every sim card carrier has own APN content, we have two methods to find out apn content : check sim card carrier on internet or put sim card into cell phone to find out APN
Set apn by sending command “apn123456 content” , “apnuser123456 content” ,“apnpasswd123456 content” pls note the content is from SIM card carrier , there is small blank after 123456 in every command.

# COMMAND INSTRUCTION TO SET APN

| INSTRUCTION | COMMAND | REPLY |
| --- | --- | --- |
| Set APN ( any existing will be replaced) | apn+123456+space+apn content | apn ok |
| Set APN username | apnuser+123456+space+content | apnuser ok |
| Set APN password | apnpasswd+123456+space+content | apnpasswd ok |

E.g:

For vodafone mobile SIM card in Germany, we got APN information below.

APN name:web.vodafone.de

APN username:vodafone

APN password:vodafone

Send SMS to set apn below

1. apn123456 web.vodafone.de

2. apnuser123456 vodafone   (no need to set if without apnuser)

3. apnpasswd123456 vodafone  (no need to set if without password)

4.2 WEBSITE  TRACKING

# Platform : www.mytkstar.net

Select “Log in by IMEI” on the bottom of screen

# ID No. : on the back side of cover

Password: 123456

4.3APPLICATIONS FOR ANDROID/IOS

Search “TKSTAR GPS“ in the Apple App Store/Google Play

Store or Scan the QR Code to install the applications on

your cell phone.

4.3.1 Login by IMEI/ID (Only one tracker)

Select “Log in by IMEI/ID” on the bottom of screen

# Server:  www.mytkstar.net

# ID : on the back side of cover

Password: 123456

4.3.2 login by username

Note: If you have two tracking devices or more, you need to contact the seller customer service first to create an account for your devices. You can login by username when you get a username and password.

Select “Log in by username” on the bottom of screen

Server: www.mytkstar.net

username:contact the seller customer service to create it

Password:123456

4.3.3 Real-time tracking

Real-time tracking not only can track the position of the device, but also can track the position of smart phone

On map click "+" and "-" to zoom in and zoom out the map.

Click "" to view different location between smart phone and device,

and click "" to change the map vision between 2D/3D.

EXPLANATION OF OTHER ICONS IN APP:

Historical route: It could find the route map for nearly six months by choosing the beginning and ending time.

Geo-fence: It will generate an alarm on App when the device is out of the Geo fence you set.

Issue: Issue commands to the device.

Device info: The information of device.

Device message: The alert message generated by the device.

OBD : For customers to detect vehicle failure and vehicle status.

User Info:The information of account.

Alarm setting: Turn on/off the different alarm types for the device.

5. Notices:

1.GPS tracking can be worked outdoor.

2.Please make sure SIM card supports making calls, sending messages, GPRS network.

3.Please make sure SIM card is with sufficient balance.

4.Please make sure the SIM card has opened the call shows and turned off the call transfer.

5.Do not assembly and disassembly device at will.

6. FAQ and processing methods.

| FAQ | Instructions/Solutions |
| --- | --- |
| Fail to turn it on | Please check if battery is charged.The device is automatically charged & turned on when it is plugged into the OBD port. |
| No SIM signal | Please check if SIM card installed correctly. Don’t turn on the PIN code Please check if the device is correctly inserted into the OBDII port. Please check if voltage of the power is normal 电源电压是否正常 |
| No GPS | A more open view of the sky is recommended to make sure the device can receive the GPS signal normally. |
| No reply to SMS command | The command format is wrong or insufficient SIM card balance. |
| SMS position OK, cannot use the APP and web platform | Pls check if APN is correctly set. And pls find out the correct APN content of the SIM card. (Pls refer to 4.3 setting.) |
| OBDII data read is incomplete or inaccurate | This related to the car model,some car models only open to read part of their data. If there is a car model that cannot read all data, you can contact the seller customer service and provide information of the car model and ID number for remote development and upgrades. |