### BD/GPS Tracker Terminal

### Quick

### Installation

User

Manual

(Version V1.1)

Thank you very much for using GPS TRACKER, the user manual will guide how to operate this product, please read it carefully before using it in order to get the correct method of operation. If the appearance, color and accessories of this product are modified, please refer to the actual product. The manufacturer is not liable for faults and omissions which in the user manual.

- Product functions & Parameters

1.1 Product functions

Location inquiry, geo-fence, vibration alarm, over-speed alarm, historical route playback, remote monitor.

1.2 Parameters

●QUECTEL EC20 module (different modules for different countries, the following are the frequency bands for EC20, different countries with different modules and frequency)

4G:LTE FDD:B1/B3/B5/B8

LTE TDD：B34/B38/B39/B40/B41

3G :WCDMA:B1/B8

:TD-SCDMA:B34/B39

2G :CDMA:BC0  900/1800MHz

●Wide voltage input range: 3.4- 4.5V;

●Location time: average warm start:≤3sec(open sky)

Average cold start:≤35sec(open sky)

●Device dimensions: 73.8mm × 69mm × 26.5mm (5000mA);

73.8mm × 69mm × 35.5mm (10000mA)

●Location accuracy:≤10 meters;

●Working Temp:-20℃ - 75℃

2、Product accessories and LED light status

2.1 Product accessories:

Standard: the device/ charging cable / quick installation user manual / double-sided stickers

Optional: powerful magnetic

2.2 Device LED light status

2.2.1 Red LED (Power supply/Charging indicator)

| Light status | Meaning |
| --- | --- |
| light | charging |
| off | Finished/not charging/Power off |

2.2.2 Yellow LED(GSM signal)

| Light status | Meaning |
| --- | --- |
| Quick flash 1 time within 2 seconds | GSM initialization |
| light | GPRS normal communication/online |
| off | GSM sleep/power off |

2.2.3 Blue LED (GPS signal)

| Light status | Meaning |
| --- | --- |
| Quick flash 1 time within 2 seconds | GPS signal searching |
| light | GPS location finished |
| off | GPS sleep/power off |

- Installation instructions

3.1 Preparation before installation:

1, Open the box and check whether the device and the accessories are complete, otherwise please contact your dealer.

2, SIM card selection, the device works with Micro SIM card, and support full Netcom band.

3, SIM card installation, there is a small back cover on one side of the terminal, push out the small back cover, pick up the metal cover of the SIM card slot, put the SIM card chip down into the card slot, and cover the metal cover of the card slot.

Note: (1) Before installing or removing the SIM card, please switch off the device;

(2) Should activate the GPRS function of the SIM card;

(3) Should activate the caller ID function; (activate or not according to the functions you chose.)

(4) If your SIM card required you to input the SIM PIN, please refer to your mobile phone user manual to turn off the SIM PIN function.

(5) Please ensure that the SIM card is valid.

3.2 Installation

We recommend a hidden installation, and we suggest that you ask a professional organization designated by the dealer. Please note the following:

1, Hidden installation, pay attention to waterproof;

2, Do not put together with the launch source, such as reversing radar, anti-theft device or other in-vehicle communication equipment;

3, GSM antenna and GPRS antenna were built-in the device, make sure that the GPS receiving surface (GPS antenna surface without label) is upward (toward the sky), and there is no metal shielding on the top.

Recommended installation location:

(1) Inside the decorative frame under the front windshield of the car;

(2) Areas around the front dashboard of the car (non-metallic material surface);

(3) Under the decorative plate of the rear windshield of the car;

(4) Inside the car door or the middle column;

(5) Inside the instrument panel or under the rear seat of the electric bicycle/motorcycle

4. Proper use of the product: Installation → Switch on → Settings → Register

Installation: When installing, the GPS antenna surface should face the sky. There should be no electromagnetic wave absorber (such as metal or explosion-proof film).

Switch on: Insert the SIM card with right direction, connect the cable according to the wiring diagram, and then switch on the device.

Register platform account: The registration method varies according to the dealer's platform, please consult the dealer.

5. SMS commands and instructions:

Send SMS command from user’s SIM card number to the SIM card number which inside the GPS device.

The commands in the following SMS command list are in English input format, and the letters are case-sensitive according to the instruction requirements.

| Common inquiry | SMS command format | Device reply |
| --- | --- | --- |
| Center number setting | 101#13712345678# | OK |
| Device status query | CXZT | Version, ID, IP, etc… |
| Reset the device | CQ | system reset OK! |
| Restart GPS | CQGPS | GPS reset OK! |
| Restore factory settings | FORMAT | OK |
| APN setting | apn123456 cmnet | SET APN OK |
| APN user name | apnuser123456 user | SET APNUSER OK |
| APN password | apnpasswd123456 password | SET APNPASS OK |
| ignition/motion upload interval | freq,123456,20 | OK |
| Revise Server IP | IP+blank+IP+blank+port Example：IP 106.3.230.234 8185 | set IP OK |

6. App operation

Login location service platform

Users can login to the global positioning service platform provided by the dealer, to check the location and status of the vehicle, and perform corresponding operations. Please consult your dealer for the service platform website.

Platform login on computer:

For individual users, please login with the device ID number. The ID number is on the device body and also on the package box. When logging in to the platform, please select IEIM/License number to log in. The default password is: 123456

Enterprise users and fleet users please select the username to log in. User name and password are set by the dealer, please contact your dealer for distribution!

Android APP download, please scan the QR code on the computer, and if Apple mobile phone, please search the APP name in the App store.

Login page operation introduction

Login and add the device into the device list, then you enter the  app home page, users can check battery level, location time, motion status, motion direction, speed, address resolution and other information of the device. Click on “Real Time Tracking”, “Historical route” etc…

Real-time tracking operation introduction

Real-time monitoring: Click the “Real-time Tracking” icon to enter the corresponding page, then can check the vehicle running status, driving route, speed, direction and other information in real time.

Historical route: Playback of the historical route of the device on a certain day or a period of time (suggest no more than 7 days, otherwise the amount of data loaded will be too large)

Click "Select Date" to pop up the calendar: IOS long press on the calendar to enter the multi-day selection mode and that day is the start date, press and hold another day as the end date to view the historical track during the period; Android click and select the range and click on the right

Introduction of commands

Vibration alarm on: if this command sent successfully, if there are vibration, will receive alarm message.

Vibration alarm off: Turn off the vibration alarm function.

Main control number: Receive alarm call, alarm SMS.

S O S number: Receive SOS cal, if the device support.

Pass-through: Send SMS commands through the APP.

Smart mode: upload data according to the pre-set time interval, other time does not work, device will not upload position even though vibration.

Normal mode: if there is vibration or movement, the data is uploaded every 30 seconds (default). Without vibration or movement, the device automatically enters into the power saving mode, the GPS is turned off, and the device is not offline.

Power saving mode: no vibration or movement, the device automatically enters into the power saving mode, turns off GPS and GPRS, and the device is offline.

Voice control recording: no

Simultaneous Location: no

Upload interval: Set the working status upload interval (unit: second), the default interval is 60 seconds.

Remote restart: The device will restart automatically after clicking the command.

Remote shutdown: no

7、Trouble shooting

If the device can’t be connected to the background server after first time installation, and the background server shows it is offline, please check the installation correct or not.

If you have any questions for the operation, please refer to the following questions and solutions; if you still can't solve the problem, please contact your dealer.

| Common Problems | Reasons | Solutions |
| --- | --- | --- |
| Poor signal | Test at areas where there are high buildings or underground parking lots, where radio waves cannot be sent or received normally. | Use it at a good signal place |
| platform shows device not activated after first installation | Main power supply connected correct or not | Do not connect to the main control line of the vehicle |
|  | SIM inserted not correct | Check the SIM card |
|  | LED status | Check if the indicator is blinking or steady |
|  | SIM without GPRS activated or SIM card out of charge. | Please contact carrier to activate GPRS or charge |
| Platform map shows incorrect location | GPS no location | Please go to outdoor place where GPS signal good |
|  | Vehicle did not move after installation | Please drive the vehicle on the road |
|  | ACC connected or not | Connect the device and turn on ACC |
| Platform shows the main power disconnect | Poor power supply connection | Check whether the power supply line of the device connected correct or not |
| Platform shows device offline | SIM card out of charge of GPRS was canceled | Please check your SIM card |
|  | Weak signal area | Please try again at good signal area |

Warranty card

Special statements:

1. If there is any technical modification for this product in the future, no further notice.

2. If the appearance or color of the product were changed, please refer to real product.

3. The warranty card is only applicable to product with IMEI number listed as below.

4. Please keep this card in good condition. Please present this card and the original purchase receipt when you apply warranty.

5. Please refer to the table below for the warranty range.

This card is the basic proof of the warranty. Please fill in the card carefully and keep it in good condition.

| User Name |  | Telephone Number |  |
| --- | --- | --- | --- |
| Address |  |
| Model No. |  | IMEI |  |
| Purchasing Date |  | Commercial invoice No. |  |
| Seller Name |  |
| Seller Address |  |
| Seller contact number |  |
| One year from the date of purchase, the non-human damage failure is guaranteed for one year; Any of the following conditions is not covered by the warranty, but can be repaired if you pay the cost (1) Exceeding the warranty period; (2) Damage caused by unauthorized disassembly or repair without the authorization of our company; (3) immersed in water and the circuit board was burnt; (4) Damage caused by improper installation, use, maintenance or storage; (5) damage of outer casing caused by the improper use; (6) The IMEI number of the product is torn or blurred; (7) The warranty card and product model No. not match, or the warranty card was altered; (8) Damage caused by force majeure. |

### 北斗/GPS定位终端

### 快

速

使

用

指

南

(版本V1.1)

非常感谢您使用GPS TRACKER，使用指南将详细的说明如何操作本产品。请您在使用之前认真阅读，以便得到正确的使用方法。本产品外观、颜色及配件如有改动，请以实物为准。制造商对于使用指南中的过失和疏漏不承担法律责任。

- 产品功能参数

1.1 产品功能

位置查询、电子围栏、震动报警、超速报警、轨迹回放、远程拾音

1.2 性能参数

●QUECTEL EC20模组（不同国家模组有所区分，以下参数为EC20频段，不同国家使用模组不同，支持的频段不同）

4G:LTE FDD:B1/B3/B5/B8

LTE TDD：B34/B38/B39/B40/B41

3G :WCDMA:B1/B8

:TD-SCDMA:B34/B39

2G :CDMA:BC0  900/1800MHz

●工作电压输入范围: 3.4-4.5V;

●定位时间:平均热启动:≤3sec(open sky)

平均冷启动:≤35sec(open sky)

●机身尺寸:73.8mm * 69mm * 26.5mm(5000mA)

73.8mm * 69mm * 35.5mm(10000mA)

●定位精度:≤10米;

●工作温度:-20℃ 至 75℃

2、产品配件和LED灯状态

2.1产品配件:

标配:设备/充电线/快速安装指南/双面贴

选配:强磁磁铁

2.2终端LED工作状态

2.2.1红色LED(电源/充电指示灯)

| 灯的状态 | 含 义 |
| --- | --- |
| 常 亮 | 充电中 |
| 不 亮 | 充电完成/未充电/关机 |

2.2.2黄色LED(GSM信号状态)

| 灯的状态 | 含 义 |
| --- | --- |
| 2秒内快闪1次 | GSM初始化 |
| 常 亮 | GPRS通讯正常/已经上线 |
| 不 亮 | GSM休眠/关机 |

2.2.3蓝色LED(GPS信号状态)

| 灯的状态 | 含 义 |
| --- | --- |
| 2秒内快闪1次 | GPS信号搜索中 |
| 常 亮 | GPS已定位 |
| 不 亮 | GPS休眠/关机 |

- 终端安装说明

3.1 安装前的准备工作：

①打开包装盒，检查设备型号是否正确，配件是否齐全，否则请联络你的经销商；

②SIM卡选择，终端需要插入一张Micro SIM卡，全网通频段支持移动、联通、电信。

③SIM卡的安装，SIM卡缺角朝里，芯片对着有弹片的一方放入卡槽，感觉到明显的锁

卡即可。

注意：⑴ 在安装或取出SIM卡前，请先将终端的电源切断；

⑵ 终端SIM卡需要开通GPRS功能；

⑶ 终端SIM卡需要开通来电显示功能；（依据客户需要的功能选择开通或者不开通）

⑷ 若您的SIM卡已开启要求输入SIM PIN，请参考您的手机用户手册将输入SIM PIN功能关闭；

⑸ 请确保终端SIM卡有资费。

3.2 安装

终端的安装方式建议为隐藏式安装，终端设备的隐藏安装建议由经销商指定的专业机构进行安装，注意如下事项：

①隐蔽安装，注意防水；

②避免与发射源放在一起，如倒车雷达、防盗器及其他车载通讯设备；

③设备内置有GSM天线和GPRS天线，安装时应确保GPS接收面（没有标签面为GPS

天线面）向上（朝天空），且上方无金属物屏蔽。

建议安装位置：

⑴ 汽车前挡风玻璃下方装饰框内隐蔽处；

⑵ 汽车前仪表盘（表皮为非金属材质）周围隐蔽处；

⑶ 汽车后挡风玻璃下方饰板下；

⑷ 汽车门内或者中柱内；

⑸ 电动车/摩托车仪表盘内或者后座下面隐蔽处。

产品的正确使用步骤：安装→开机→设置→注册

安装：安装时，应使GPS天线面朝向天空，安装位置上方必须是没有电磁波吸收的物质（如金属、防爆隔热膜）遮挡的地方。

开机：按正确方向装上SIM卡，按终端接线示意图接好线，然后拨动电源开关开机。

注册平台帐号：注册方法依据经销商的平台不同，注册方法也不相同，请咨询经销商。

6、短信指令说明及使用方法：

用户SIM卡号发送短信指令给GPS车载通讯终端SIM卡号。

以下各短信指令格式中的逗号为英文输入状态格式，字母按指令要求分大小写。

| 常用查询功能 | 短信指令格式 | 设备回复 |
| --- | --- | --- |
| 中心号码设置 | 101#13712345678# | OK |
| 终端状态查询 | CXZT | 版本、ID、IP等信息 |
| 重启设备 | CQ | system reset OK! |
| 重启GPS | CQGPS | GPS reset OK! |
| 恢复出厂设置 | FORMAT | OK |
| APN设置 | apn123456 cmnet | SET APN OK |
| APN对应的用户名指令格式 | apnuser123456 user | SET APNUSER OK |
| APN对应的密码指令格式 | apnpasswd123456 password | SET APNPASS OK |
| 点火运动上传时间设置 | freq,123456,20 | OK |
| 服务器IP修改设置 | IP+空格+IP地址+空格+端口号 例子：IP 106.3.230.234 8185 | set IP OK |

- 设备应用操作

登录位置服务平台

用户可登录经销商提供的全球定位服务平台来查看车辆的位置、状态，并进行相应的操作，服务平台网址请咨询您的经销商。

电脑登录查平台方法：

个人用户请用设备ID号码登录，ID号码在设备机身，和包装盒子上，登录平台的时候请选择，IMEI/车牌号登录。密码出厂默认为：123456！

企业用户和车队用户请选择用户名登录。用户名，密码由经销商设置，请联系各自经销商分配！

安卓APP扫描电脑上面二维码扫描下载，苹果手机在苹果应用市场搜索APP名称下载。现在个人用户请用设备ID号码登录，ID号码在设备机身，和包装盒子上，登录平台的时候请选择，IEIM/车牌号登录。密码出厂默认为：123456！

企业用户和车队用户请选择用户名登录。用户名，密码由经销商设置，请联系各自经销商分配！

登录界面操作介绍

登录成功且添加设备后，即进入APP首页地图。通过设备气泡框，用户可查看该设备的：剩余电量，定位时间，运动状态，运动方向，速度，地址解析等信息。点击“实时监控”，“历史轨迹”，“更多”可快速进入相应的功能页面

实时跟踪操作介绍

实时监控：点击“实时监控”图标进入相应页面，实时查看车辆运行状况、行驶路线、速度、方向等信息。

历史轨迹：回放设备某一天或一段时期内（建议不超过7天，否则加载数据量会过大）的历史轨迹

点击“选择日期”弹出日历：IOS长按日历上某一天则进入多天选择模式且该天为开始日期，按着长按另一天作为结束日期，查看该段时期内历史轨迹；安卓则单击选择范围即可点击右

命令下发操作介绍

振动报警开：命令下发成功，设备振动APP会产生报警。

振动报警关：关闭振动报警功能。

主 控 号码：接收报警电话，报警短信。

S O S 号码：接收求救报警，需要设备支持。

透      传：通过APP下发短信命令。

智 能 模式：智能模式，按下发时间间隔工作，其它时间不工作，振动也不会上传定位数据。

正 常 模式：终端出厂默认模式，有振动或者移动的情况下每30秒（默认）上传一次数据，没有振动或者移动，设备自动进入省电模式，关闭GPS,设备不离线。

省 电 模式：没有振动或者移动，设备自动进入省电模式，关闭GPS和GPRS,设备离线。

声 控 录音：无

即 时 定位：无

上 传 间隔：设置工作状态上报间隔（单位：秒），默认60秒一条。

远 程 重启：点击指令下发成功后设备会自动重启。

远程开关机：无

8、故障排除

8.1 终端首次安装后一直无法连接至后台服务器，后台显示未上线。请检查终端安装：

在操作终端时，如果感到不正常，请参阅下列问题及解决方案；若仍不能解决问题，请与经销商取得联系。

| 常见问题 | 发生问题 | 解决办法 |
| --- | --- | --- |
| 信号接收不良 | 在接收不良的地区使用终端，如高楼附近或地下停车场，无线电波无法有效传达 | 位于信号良好的位置使用终端 |
| 首次安装平台显示 未启用 | 主电源线接线是否正确 | 不要安装到汽车内部控制线上 |
|  | SIM卡未装好 | 检查SIM卡 |
|  | LED指示灯状态 | 查看指示灯是否闪烁或常亮 |
|  | SIM卡未开通GPRS功能 | 请联系服务商开通GPRS |
| 平台地图显示 位置不正确 | GPS未已定位 | 请到室外空旷的地方进行定位 |
|  | 终端安装好后车辆静止不动 | 把车开到路上跑几圈 |
|  | ACC线是否有接 | 接好终端插入车钥匙打开ACC |
| 平台显示主电断开 | 电源线接触不良 | 检查设备电源线是否连接好 |
| 平台显示离线状态 | SIM卡欠费或被取消GPRS | 请检查SIM卡状态 |
|  | 掉线区域信号弱 | 请到信号强的地方重试 |

保修卡

特别声明：

- 若本产品日后有任何技术变更，恕不另行通知。

- 产品外观、颜色如有改动，以实物为准。

- 保修卡只适用于下述所列IMEI号机子的三包服务。

- 请妥善保管此维修卡，保修时请出示此卡及原购买单据。

- 具体保修范围请参见下表说明。

此卡为保修的基本凭证，请用户认真填写此卡并妥善保存。

| 用户姓名 |  | 联系电话 |  |
| --- | --- | --- | --- |
| 通讯地址 |  |
| 产品型号 |  | IMEI号 |  |
| 购机日期 |  | 发票号码 |  |
| 销售单位名称 |  |
| 销售单位地址 |  |
| 销售单位电话 |  |
| 自购买之日起，非人为损坏故障保修一年； 属于下列情况之一的，不在保修范围内，但可付费维修； 超过保修期限； 未经我司授权，擅自拆卸或维修造成损坏； 浸水，电路板烧毁； 因安装、使用、维护、保管不当造成损坏的； 使用过程中引起的产品外壳损坏； 产品内部IMEI号被撕去或模糊不清； 保修凭证与产品型号不符或保修凭证被涂改； 因不可抗力造成的损坏。 |