GPS

User Guide

(version 3.0)

Please read carefully before using the installation guide to get the correct installation and operation, product appearance and color are subject to change, please prevail in kind!

Contents

1. Product Accessories	3

2. Product Features	3

3. Installation Notes	3

3.1 Preparation Before Installation	3

3.2 Installation	4

3.3 Terminal Outlet Defined	4

3.4 Proper Use of The Product	4

3.5 Indicators	5

4. Instructions	5

4.1 Owner password settings	5

4.2 Set a SOS specific number	5

4.3 No Power Alarm Set	6

4.4 ACC Security Settings	6

4.5 Vibration Alarm Settings	7

4.6 SOS Alarm Settings	7

4.7 Remote monitoring	8

4.8 Voice intercom (Optional)	8

4.8 SMS Text Query Location Information	8

4.9 Speed Alarm Settings	8

4.10 Move Alarm Settings	8

4.11 SMS armed and disarm settings	9

4.12 SMS Off Fuel (Optional)	9

4.13 GPS Reboot	9

4.14 GPS Reset	9

4.15 Device Reboot	9

4.16 Query Device Information	9

4.17 APN Settings	9

4.18 Setting the server IP and port:	9

4.19 Platform Application	9

5. Troubleshooting	10

6. Warranty	11

# Product Accessories

1.1 Power cable

1.2 User Guide

1.3 Microphone (optional)

1.4 SOS button (optional)

1.5 Relay (optional)

# Product Features

2.1 GSM850 / 900 /1800 / 1900MHZ quad-band systems worldwide;

2.2 Wide operating input voltage range: 9-80VDC;

2.3 GPS / LBS real-time positioning, support the computer to track the car, mobile search vehicles and wechat search vehicles;

2.4 Support SMS text query location information;

2.5 ACC ignition signal is detected, the vehicle prompted the state;

2.6 Built-in vibration sensor, to achieve intelligent vehicle anti-theft;

2.7 Able to set a specific number for SOS alarm and burglar alarm;

2.8 SOS switch button for emergency call for help;

2.9 Internal / external microphone and speakers, remote audio monitoring and voice intercom function (optional);

2.10 Built-in backup battery, to achieve illegal cutting wire alarm (optional);

# Installation Notes

## 3.1 Preparation Before Installation

3.1.1 Open the box, check is the equipment correct, are accessories complete, otherwise please contact your dealer;

3.1.2 SIM card selection, the terminal needs to insert a GSM SIM card, GSM card Unicom mobile or optionally (GSM networks worldwide)

3.1.3 SIM card installation, open the terminal device, take off the metal cover SIM card slot, SIM card chip insert into the slot, covered with a metal slot cover.

Note: (1) Before installing or removing the SIM card, first turn off the device power;

- Terminal SIM card need to open GPRS function;

- Terminal SIM card need to open the Caller ID function (depending on customers prefer or not);

- If your SIM card needs to enter SIM PIN, please consult your phone's user manual to turn off SIM PIN;

- Make sure that the SIM card has charges;

## 3.2 Installation

Terminal installation is concealed installation, hidden installation recommendations terminal equipment designated by the distributor of professional and technical personnel to install, note the following:

3.2.1 To avoid damage to the thief, the device select bits should be hidden;

3.2.2 To avoid to put the emission sources together, such as reversing radar, anti-theft devices and other automotive communications equipment;

3.2.3 It can be fixed by cable ties, or use wide sponge double-sided adhesive stickers;

3.2.4 Equipment built-in GSM antenna and GPS antenna, the installation should ensure a positive upward (toward the sky), and the above non-metal shield block, the proposed installation location:

- Below the windshield inside the decorative panel;

- Car meter (surface of non-metallic materials) around the shelter;

- Rear windshield below the decorative panel;

- Inside car door or pillar;

- Within the dashboard or under back seat hidden

Note: (1) If below the windshield there is metal insulation or heating layer will reduce the GPS signal reception, causing the GPS malfunction, please change the installation position;

- Some models are built-in 3D sensor, and it needs to detect acceleration, deceleration and rollover, equipment must be installed according to the mounting direction front and rear direction of the vehicle can not be mounted transversely.

## 3.3 Terminal Outlet Defined

- Red line connects positive power;

- Black line connects negative power;

- Orange connects ACC;

- Yellow connects relay

Please use the original supplied power cord, the red line is the positive power supply, black for negative power, negative power installation, choose a separate grounding or connect metal, do not connect with the other ground wire together. If need ACC automatic anti-theft function, ensure to connect the ACC line, the device will detect the ACC state to decide whether to enter the security mode; If not connect to ACC line, the vehicle will enter the security mode, vibration occurs under the security mode, vibration alarm will be triggered.

## 3.4 Proper Use of The Product

Install→Power on→Settings→Register

Installation: GPS antenna should be facing toward the sky, above the mounting location must be no material (such as metal, window film) absorption of electromagnetic waves sheltered place.

Boot: Insert the SIM card correctly, connect the wire according to diagram, then turn on the power.

Setting: Must be done, or can not do other operations, mobile phone owners send text messages to set the owner number and a specific number to the terminal SIM card.

Registration: Registration method is different subject to dealer platforms, please consult your dealer.

## 3.5 Indicators

3.5.1 Red light - Power Indicator / OBD Work Lights

| LED Status | Meaning |
| --- | --- |
| Flash once in 2 seconds | Normal operation / OBD working properly |
| No light | Shutdown / OBD sleep |

3.5.2 Yellow indicator light -GSM

| LED Status | Meaning |
| --- | --- |
| Flash once in 2 seconds | GSM initialization |
| Light Always | GPRS is normal / already online |
| No light | GSM sleep |

3.5.3 Blue LED light -GPS

| LED Status | Meaning |
| --- | --- |
| Flash once in 2 seconds | GPS signal searching |
| Light Always | GPS targeted |
| No light | GPS sleep |

# Instructions

Note: The symbol is separated by a comma, the following function parameters instruction comma is in English input state.

## 4.1 Owner password settings

Owners can only bind one mobile number, the last mobile number of binding is effective. bind a certain mobile number, other mobile number can not be reached or connected.

The default owner password is: 123456

Set owner number is: admin123456 13712345678

Re: Welcome and thank you for choosing Poronix GPS tracker, admin ok

Modify owner password: password123456 666888 (666888 for the new password)

Re: password ok

## 4.2 Set a SOS specific number

Specific number for the alarm number, , you can send an SMS instruction to add SOS number, you can add two specific number SOS, 101 is the default owner number, 102 for the first SOS specific number, 103 for the second SOS specific numbers, in the alarm state, the device will send location information or SOS to a specific number (information is based on whether the set needs), and the cycle call until the dial up. Before setting specific numbers, all numbers can be set and query. After set a specific number, without a password can only be associated with the specific number set.

4.2.1 Add specific numbers

Instruction format: 102#number#

E.g. 102#13712345678#

Reply message: OK

4.2.2 Delete a specific number

Instruction format:

D101#

D102#

D103#

Example: D101# means to delete the first number.

Reply message: OK

4.2.3 Query a specific number

Instruction format: C10#

Example: C10#

Reply message: 101#13712345678

102#13712345688

103#13712345698

## 4.3 No Power Alarm Set

4.3.1 Turn on no power SMS alarm: pwrsms123456,1

Re: pwr sms alarm set ok

4.3.2 Turn off no power SMS alarm (default): pwrsms123456,0

Re: pwr sms alarm set ok

4.3.3 Turn on no power phone call alarm: pwrcall123456,1

Re: pwr call alarm set ok

4.3.4 Turn off no power phone call alarm (default): pwrcall123456,0

Re: pwr call alarm set ok

## 4.4 ACC Security Settings

Need to correctly connect the ACC wire

4.4.1 ACC under open status (car key turn switch on), if automatically security, turn on ACC can exit security. If security manually through SMS or platform, turn on ACC can not exit security automatically.

4.4.2 ACC under close status (car key switch off), after 3 minutes it will enter security automatically.

4.4.3 SMS settings ACC auto security on (default)

ACCLOCK,123456,1

Re: OK

4.4.4 SMS settings ACC auto security off

ACCLOCK,123456,0

Re: OK

4.4.5 SMS settings auto security time (default 3 minutes)

ACCLT,123456,3

(3 means after 3 minutes auto security)

Re: OK

## 4.5 Vibration Alarm Settings

4.5.1 Open vibration alarm SMS: 125#

Reply message: OK

4.5.2 Close vibration alarm SMS (default): 126#

Reply message: OK

4.5.3 Open vibration alarm phone call: 122#

Reply message: OK

4.5.4 Close vibration alarm phone call (default): 121#

Reply message: OK

4.5.6 Setting the duration of vibration alarm, 1-15 seconds

SMS: vibtime123456,n

Re: vibtime set ok

n(0-15) 0 cancel vibration alarm, default value is 3 seconds, 3 seconds vibration alarm

ACC auto security vibration alarm instruction: connect power, ACC shut down (car key switch off), after 3 minutes auto security, car shake illegally not turn on ACC within 5 seconds, device will send vibration alarm SMS.

If turn on vibration alarm phone call, device will call owner, owner can answer the call to listen the car situation.

Not connect ACC, can text SMS to enter or exit car security.

## 4.6 SOS Alarm Settings

When in emergency situation need help, you can press the SOS to trigger SOS emergency alarm. Device will send a SOS message to specific number and call the specific number until pick up. Device will also send SMS alarm information to platform.

Note: SMS and phone call alarm function need to set a owner number at first, SOS phone call and SMS function need to set a specific SOS number.

4.6.1 Turn on SOS SMS alarm

sossms123456

Re: sossms ok

4.6.2 Turn off SOS SMS alarm (default)

no sossms123456

Reply: no sossms ok

4.6.3 Turn on SOS phone call

soscall123456

Re: soscall ok

4.6.4 Turn off SOS phone call (default)

no soscall123456

Reply: no soscall ok

## 4.7 Remote monitoring

Specific number can monitor GPS device SIM card number

SMS:88

Note: Need to set the owner number and SOS specific number at first

## 4.8 SMS Text Query Location Information

4.8.1 When you need to query the terminal device location information, you can text messages send to the SIM card on the device, the device will reply the last location.

SMS: 123

4.8.2 Owner number call the device reply location information, ring twice then hang up.

4.8.3 Google Link SMS: g1234

## 4.9 Speed Alarm Settings

Overspeed alarm SMS Speed Limit:

speed123456 080

Setting the speed limit of 80 km / h

4.9.1 Turn off speed alarm SMS (default)

speed123456 000

Re: speed ok

4.9.2 Turn on speed alarm SMS

speed123456 080

Re: speed ok

## 4.10 Move Alarm Settings

Move alarm setting instructions: move123456 300

Re: move ok

Unit: meter

Under alarm situation GPS reply: move alarm!  GPS security off

Move alarm cancel (default): move123456 000

Re: move ok

## 4.11 SMS armed and disarm settings

SMS armed: SF

Re: SF OK

SMS disarm: CF

Re: CF OK

## 4.12 SMS Off Fuel (Optional)

When the vehicle thefts, by monitoring background to send off fuel directive, to ensure the vehicle is in safe driving premise, cutting stolen vehicle fuel, unable to start the vehicle to achieve the purpose.

NOTE: To ensure the safety of vehicles, the terminal is active only in the GPS targeting state, and the vehicle speed is less than 20KM / H or stop to cut off fuel.

When theft alarm is over, you can restore fuel manually through background, terminal performs recovery operation, the vehicle will continue to travel.

SMS fuel off: DY

SMS fuel on: KY

## 4.13 GPS Reboot

SMS: CQGPS

## 4.14 GPS Reset

SMS: FORMAT

## 4.15 Device Reboot

SMS: CQ

## 4.16 Query Device Information

SMS: CXZT

## 4.17 APN Settings

Set APN: apn123456 cmnet

Re: apn ok

Set APN user name: apnuser123456 user

Re: apnuser ok

Set APN password: apnpasswd123456 password

Re: apnpasswd ok

## 4.18 Setting the server IP and port:

SMS modifications: szcs,123456,domain=106.003.230.234:8185

SMS format: IP+ space+ IP address+ space+ port number

E.g. IP 219.143.106.193 8500

Re: set IP OK

## 4.19 Platform Application

The dealer platforms are different, please consult your dealer internet website

4.19.1 Real-time monitoring, network / phone search vehicles

GPS + LBS dual-mode positioning, GPS positioning accuracy of 2 meters, when GPS has signal use GPS positioning, in a place with no GPS signal use LBS base station to locate, dual-mode automatic switching, let your GPS vehicle positioning terminal communication always online, make sure you monitoring 365 days x 24 hours always online.

Real-time phone monitoring: mobile login domain.

Real-time platform monitoring: computer login domain.

4.19.2 Track Playback

Login platform, click on the historical track playback function.

4.19.3 Statistics Report

Logistics companies can be set by the software to monitor the goods is notified of the departure time, route point, line alarm, warning area, heavy hit the alarm, rollover warning, driving speed, etc., we will comprehensive analysis of goods in transit situation and issue reports.

Login platform, click statistics report

4.19.4 Windows, Android, Ipad, Iphone, Wechat client please go to auto download service platform, each client application please contact customer service.

# Troubleshooting

5.1 If the terminal is unable to connect to the background server in the first time installation, background shows offline, please check the terminal installation

5.1.1 Check is the main power connection correct, pay attention not to connect to the vehicle interior control wire.

5.1.2 Is SIM card installed correctly, please refer to the installation instructions.

5.1.3 Please check is it power on, the switch at the back cover.

5.1.4 Check the LED status, please refer to the indicators instruction.

5.1.5 Check whether the GPS has been positioning, if not please go to the open air for the first time targeting.

5.2 Terminal shows offline in the background

First check equipment three lights are they normal, in the absence of conditions to check the lights situation, you can check the status of the SIM card, follow these steps:

5.2.1 Call the SIM card number of the device, see if you can hear the sound of the call is connected.

5.2.2 Whether the vehicle is in the basement does not have the GSM network signal.

5.2.3 Observation offline region, individual or all offline, to check whether the operator's network problems.

5.2.4 Is SIM card no charges.

5.2.5 Whether GPRS service is canceled (by the end of the month).

5.2.6 Query parameter settings, view the GPRS transmission time interval is correct.

5.3 If the terminal GPS function has been activated, but for a long time does not locate, check the terminal installation position meets the requirements, please refer to the installation instructions.

5.4 When in the poor GPS signal reception environment (surrounding tall buildings block the GPS signal), please drive to the open air to locate, generally the first time targeting needs 1-2 minutes.

5.5 When specific number receive power off SMS, check whether the illegal cutting line, otherwise check the power line fuse is broken, if so please contact your dealer to replace the same types of specifications FUSE. After exclusion of the terminal and check internal fault, then we can turn on power to let the GPS continue to work.

# Warranty

In particular that:

- Any technical changes to the product in the future without prior notice.

- Any changes of appearance, color of products, to prevail in kind.

- The warranty card is only available in the following listed IMEI / ID Number warranty Services.

- Please keep this service card, please show this card and the original purchase receipt for warranty.

- See the table below illustrate specific warranty.

This card is a basic warranty certificate, user please fill out the card and keep it.

| Name |  | TEL |  |
| --- | --- | --- | --- |
| Model |  | IMEI/ID NO. |  |
| Purchase Date |  | Invoice NO. |  |